## Slide 1
Electronics and Robotics Club
Introduction to
Arduino

## Slide 2
Electronics and Robotics Club
Introduction to
Arduino

## Slide 3
Basics of Arduino
01
Arduino is a small controller that you can use to create all sorts of cool and fun projects.
An Arduino is like your little smart friend. You write a set of instructions in a special language
that it understands (code), and then you upload that code to the Arduino. Once it has the
instructions, it starts doing whatever you told it to do.
Let's say, we have to sense some movement. A motion sensor can be attached to it and it
will send data to Arduino. Now, this data can be used to control a motor controlled door.

## Slide 4
Pinout
Diagram

## Slide 5
What do the various pins do?
02

## Slide 6
USB-in: You connect your Arduino to
the laptop through this.

## Slide 7
Digital pins: Used to input/output digital
signals.
Built-in LED: Digital-pin 13 by default has an
LED attached to it, which glows
when you give power to this pin.

## Slide 8
Voltage pins: 5V (VCC), GND (ground), 3.3V. These are
power sources which provide fixed
voltage to your circuit.
Analog pins: Used to input/output analog
signals.

## Slide 9
Some other
Basic components
03
We’ll explore how to use basic components, such as LEDs and breadboards, to create basic circuits with Arduino.

## Slide 10
1. Breadboard

## Slide 11
2. LED
Anode
VCC
(Voltage Common Collector)
Cathode
GND
Ground
3. Wires
Male to Female
Female to Female
Male to Male

## Slide 12
Arduino IDE
IDE (Integrated Development Environment) is an official software by Arduino.cc used for writing, compiling, and uploading code to Arduino boards.
Arduino is similar to regular C++, with additional libraries for specific board functions.

## Slide 13
Let’s do hands-on practice by doing some tasks………

## Slide 14
Let’s do hands-on practice by doing some tasks………

## Slide 15
Task 1: Blink the LED
Let's explore how to make an LED blink using an Arduino. Here is the code you'll need to complete this task.

## Slide 16
Connect VCC and GND through a resistor as shown
Task 1: Blink the LED

## Slide 17
Play around with the delay values!!

## Slide 18
How does IR sensor Work?
The Infrared emitter first emits an infrared signal. The signal then hits the obstacle in front of it.
01
02
OUTPUT
IR EMITTER
IR RECEIVER
The reflected signal is detected by the IR receiver which then generates an output through the OUT pin.
WALL / OBSTACLE
VCC
GND

## Slide 19
How does LDR sensor Work?
(Light Dependent Resistor)
An LDR (Light Dependent Resistor) is a sensor that changes how much it resists electrical current based on how much light hits it. In bright light, it allows more current to flow through it; in the dark, it resists current more.

## Slide 20
LDR Pinout Diagram
VCC – Connected to power source (5V)
GND – Connected to common ground (0V)
DO – Digital Output

## Slide 21
Task 2: IR/LDR sensor
01 IR

## Slide 22
Task 2: IR/LDR sensor
02 LDR

## Slide 23
VCC
GND
Task 3 : Buzzer
In the buzzer the ground is kept connect to
the common ground always and VCC is
connected to the control pin of the Arduino
/micro-controller. When the buzzer is to be
kept silent – we provide low voltage/ground
through the pin and when we need to sound
the buzzer we provide high voltage through
the pin.

## Slide 24
Task 3 : Buzzer
Play around with the delay values!!

## Slide 25
VCC
GND
Task 3 : Buzzer
In the buzzer the ground is kept connect to
the common ground always and VCC is
connected to the control pin of the Arduino
/micro-controller. When the buzzer is to be
kept silent – we provide low voltage/ground
through the pin and when we need to sound
the buzzer we provide high voltage through
the pin.

## Slide 26
VCC
GND
Task 3 : Buzzer
In the buzzer the ground is kept connect to
the common ground always and VCC is
connected to the control pin of the Arduino
/micro-controller. When the buzzer is to be
kept silent – we provide low voltage/ground
through the pin and when we need to sound
the buzzer we provide high voltage through
the pin.

## Slide 27
Task 4 : ADC touch sensing
Detecting touch by detecting changes in capacitance on a pin

## Slide 28
Task 4 : ADC touch sensing

## Slide 29
Task 5: Capacitive touch and buzzer
Using the touch sensor and buzzer, try to create a circuit to generate a sound when the touch sensor pin is touched.

## Slide 30
Task 5
// code for task : 4
include <ADCTouch.h>
int ref ; //reference values to remove offset
int buzzerpin = 9;
void setup()
{
// No pins to setup, pins can still be used regularly, although it will affect readings
Serial.begin(9600);
pinMode(buzzerpin,OUTPUT);
ref = ADCTouch.read(A0, 500); //create reference values to
}
void loop()
{
int value = ADCTouch.read(A0); //no second parameter
value -= ref; //remove offset
if( value > 40 ){
// Serial.print("touchy ") ;
digitalWrite(buzzerpin,HIGH);
} else {
// Serial.print("NO") ;
digitalWrite(buzzerpin,LOW);
}
}

## Slide 31
ULTRASONIC SENSOR
An ultrasonic sensor uses a transducer to send and receive ultrasonic pulses that relay back information about an object’s proximity. It can tract distances of objects High-frequency sound waves reflect across boundaries to produce distinct echo patterns.

## Slide 32
HOW ULTRASONIC SENSORS WORK
It sends out high-frequency sound waves (ultrasound) and listen for the echo that bounces back. The sensor measures how long it takes for the echo to return. By calculating this time, it can figure out how far away the object is

## Slide 33
Code Snippet

## Slide 34
USES
The concept of ultrasound has wide applications. animals like bats and dolphins, produce ultrasound to travel and catch its prey.
bats use the concept of echolocation, to find its way in the dark. dolphins too find their food through echolocation.

## Slide 35
PROJECTS USING ULTRASONIC SENSORS

## Slide 36
Servo Motors
A servo motor is a precise motor that can rotate to exact angles. It has a feedback system to ensure accuracy and often includes gears for high torque in a compact size. Servo motors are rated in kg/cm, indicating how much weight they can lift at a specific distance from the shaft. For example, a 6 kg/cm servo can lift 6 kg at 1 cm from the shaft, but can lift less weight at greater distances.

## Slide 37
Motor Drivers
A motor driver is used instead of connecting a motor directly to a board to handle higher currents and voltages that motors require, which a board might not support. It also provides control features like speed regulation, direction changes, and protection against electrical issues.

## Slide 38
PROJECTS USING SERVO MOTORS

## Slide 39
DS3231 RTC
Highly accurate, Cost-effective
Counts Hours, Minutes and Seconds
Day of the Week, Day, Month and Year
Automatic compensation for leap years and months with fewer than 31 days
2 programmable time-of-day alarms
Operating voltage from 3.3 to 5V
3V battery
Temperature compensation capabilities
I2C protocol

## Slide 40
Code Snippet

## Slide 41
Feedback

## Slide 42
Scan this QR Code

## Slide 43
Thank You!