## Slide 1: ANALOG ELECTRONIC CIRCUITS COURSE PROJECT QUADRATURE DOWN OSCILLATOR

## Slide 2: THE APPLICATION OF THE QUADRATURE DOWN CONVERTER
Down converters are used to down convert high frequency RF signals to a lower Intermediate frequency(IF).
An I/Q down converter consists of two mixers: one for the I component and another for the Q component.
The I mixer multiplies the RF signal by a local oscillator signal with a phase shift of 0 degrees.(In phase component)
The Q mixer multiplies the RF signal by a local oscillator signal but with a phase shift of 90 degrees. (quadrature component)
By using quadrature down conversion, we create two versions of the down converted signal with a phase difference of 90 degrees which is used in doing the down conversion process.

## Slide 3: LT SPICE SIMULATION
CIRCUIT DIAGRAM

## Slide 4
FINAL OUTPUT
The high frequency signal (100K) is down converted to a low frequency signal (2K)

## Slide 5: QUADRATURE OSCILLATOR
CIRCUIT DIAGRAM

## Slide 6: WORKING OF THE OSCILLATOR
Initially there is no output but due to the positive feedback and the non-ideal behavior of the op-amps there is a slight perturbation.
The sine output from the inverting integrator is fed as input into the non-inverting integrator.
Sine wave will get integrated into cosine and the cosine will get integrated into sine.
To make the loop gain 1 as we don’t want amplification in every cycle because of which the output might saturate at a particular level R1C1 = R2C2 = R3C3

## Slide 7: Calculation of the fosc
V+2 = (1/C3S) / (R2 + 1/C3S) VSIN
= 1/(1+R3C3S) VSIN
From the voltage divider circuit of R3C3
VCOS = ((1 + R2C2S)/ R2C2S) * V+2
From the gain equation of the non-inverting amplifier
VSIN = ( -1/R1C1S) * VCOS
From the gain equation of the inverting amplifier
The loop gain should be 1 so that there will be no problems with the saturation of the output.
Loop gain = 1 = 1/(1+R3C3S)* ((1 + R2C2S)/ R2C2S)* ( -1/R1C1S)
R1C1 = R2C2 = R3C3 substituting this in the above loop gain equation we get
(-1/RCS )(1/RCS) = 1 = (wRC) =(2*pi*fosc *RC)
Fosc= 1 /2*pi*RC

## Slide 8: Output of Quadrature Oscillator

## Slide 9: FFT OF SINE OUTPUT OF OSCILLATOR

## Slide 10: FFT OF COS OUTPUT OF OSCILLATOR

## Slide 11: MIXER(SWITCH)
CIRCUIT DIAGRAM

## Slide 12: WORKING OF A MIXER (SWITCH)
The mixer in this circuit is biased in such a way that it will always be in linear mode. In order to do this we make the Vbias value equal to threshold voltage for Vgs>Vth condition to satisfy.
The current in linear mode Id = µnCOX(W/L) (VGS -VT) VDS
VGS = VOSC + VTH - VIN
VDS = VOUT – VIN
ID = µnCOX(W/L) (VOSC + VTH - VIN -VTH) (VOUT - VIN)
VOSC >> VIN ignoring the value of the vin wrt vosc
ID = µnCOX(W/L) (VOSC ) (VOUT - VIN)
In order to get the output as the multiplication of the VIN and the VOSC , VOUT << VIN
ID = µnCOX(W/L) (VOSC ) ( - VIN) so the current flows in reverse direction that means source and drain in the mosfet are exchanged.
Vswitchoutput = ID* RL = µnCOX(W/L) (VOSC ) ( - VIN) RL

## Slide 13: Mixer Parameters
The value of RBIAS = 1M ohm
This value is very high because
The value of Cc = 10 uF
MOSFET PARAMETERS

## Slide 14: Transient Plots for varying VIF
For fIN = 95kHz, 98kHz, 99kHz

## Slide 15
For fIN = 101kHz, 102kHz, 105kHz

## Slide 16: Mathematical form of the output of the mixer
So according to this formula there are two signals : one with a low frequency and on with high. When we pass the signal through a low pass circuit the high frequency component is getting attenuated and the the low frequency signal is outputted. That’s the reason why the output frequency of the QDC is less compared to the input.

## Slide 17
Transient and FFT Plot for fIN = 95kHz
Transient and FFT Plots for fin = 98kHz
Sine wave

## Slide 18
Transient And FFT Plots for fIN = 99kHz
Transient And FFT Plots for fIN = 101kHz

## Slide 19
Transient And FFT Plots for fIN = 105kHz
Transient And FFT Plots for fIN = 102kHz

## Slide 20
Transient And FFT Plots for fIN = 98kHz
Transient And FFT Plots for fIN = 95kHz
Cos wave

## Slide 21
Transient And FFT Plots for fIN = 101kHz
Transient And FFT Plots for fIN = 99kHz

## Slide 22
Transient And FFT Plots for fIN = 105kHz
Transient And FFT Plots for fIN = 102kHz

## Slide 23: LOW PASS FILTER (2KHz)
CIRCUIT DIAGRAM

## Slide 24: WORKING OF A LOW PASS CIRCUIT
The low pass filter allows the signals with the frequencies below the resonant frequency to pass through but attenuated the frequencies with frequencies higher than the resonant frequency
The transfer characteristics of the low pass filter is
At high frequencies the output will be very less according to the formula.
At low frequencies the output will be almost same as the input.

## Slide 25: Transient Responses
For 1kHz signal
For 10kHz signal

## Slide 26: Frequency Response

## Slide 27: Calculation for RC Filter
Values taken : R = 8.2k ohm
C = 10 nF
Cutoff Frequency = 1 / 2*pi*R*C
= 1/6.28 x 8.2k x 10n
= 1941.8983 Hz
= 2k Hz(approx.)
Vout / Vin = (1/sC )/ R + (1/sC )
= 1/ 1 + sCR
|Vout/Vin|=1/root(1+(RCω)2)
-3 dB Cut-off Frequency
|Vout/Vin| = 1/ √2 |1/√(1+(RCω)^2)| = 1/√2
1/(1+(RCω)^2) = ½
(R.C.w)^2 = 1
w = 1/RC
f = 1/2piRC

## Slide 28: Low Pass Filter Transient Plot for frequency of 1kHz

## Slide 29: Low Pass Filter Transient Plot for frequency of 10kHz

## Slide 30: THANK YOU